## Slide 1: ES-SES4000 Facility Mangement Project
Southeast University College of Norway
NovoFM team:
Badis Madani (Project Manager)
Håkon Hedlund (System Engineer)
Zhili Shao
Arshad Shakil
Prof. Aurilla Arntzen

## Slide 2: Smart Facility Management
FM is the integration of processes within an organization (like school, hotel, hospital, apartment complexes,) to maintain and develop the agreed services which support and improve the effectiveness of its primary activities.

## Slide 3
Facilities:
Schools
Office buildings
Hotels
Hospitals
Apartment complexes
Shopping centers,
Restaurants
Parking lots
Airports
Bus & Train stations
Services:
Lighting service
Fire security
HVAC (Heating, ventilation, air conditioning)
Access control (to the facility)
Energy monitoring
CCTV,..etc.

## Slide 4: Opportunity (Study case)
FM is a very complex domain.
HVAC (Heating, ventilation, air conditioning)
Indoor environment (Temperature, Humidity, Air quality)
The Goal:
Design a smart control system for HVAC services in facilities, by making it more efficient and easier to use, by 1st May 2016.

## Slide 5: Project Taxonomy

## Slide 6: WBS

## Slide 7: Gantt Chart

## Slide 8: Risk management
Type | Source | Level | Strategy | Solution
Project Risk | Lack of competence | Medium | Reduction | Do internal training and devote more human hours on research. External training.
 | Project delay | High | Prevention | Be sure that project leader follows up on the groups work. And the group has knowledge about the project delay.
Task Risk | Not compatible with current system | High | Prevention | Verify current systems and its standards
Business Risk | Solution is similar to something on the market | Medium | Prevention | Keeping track of current trends and systems on the market
Conflict Risk | Disagreement over project issues | Medium | Reduction | Collaborating, Compromising, Smoothing, Forcing, and Withdrawing

## Slide 9: Current HVAC control system

## Slide 10: Stakeholders
Defined five stakeholders
  Users
  Facility manager
  HVAC vendor
  Estate owner
  Government

## Slide 11: Survey analysis
63 people questioned, 15 were employees and the rest students
Questionnaires and online survey were used
They were asked questions about age, occupation, how satisfied they were about indoor environment, what they would want to change if they had the chance, and how they want to change it.
Results [picture showing satisfaction]

## Slide 12: Survey analysis

## Slide 13: CONOPS

## Slide 14: Design alternatives
Proposed three design concepts
  Panel controller
  Remote controller
  Mobile app controller
Selection criteria
  Initial cost
  Life-cycle cost
  Easiness of use
  Easiness of installing

## Slide 15: AHP matrix
 | Initial cost | Life-cycle cost | Easiness of use | Easiness of installing | Weighted Evaluation
Criteria Weights | 0,0799 | 0,3000 | 0,5488 | 0,0714 | 
Design Concepts |  |  |  |  | 
Panel Control | 0,2114 | 0,2390 | 0,6070 | 0,1429 | 0,4319
App Control | 0,6864 | 0,6234 | 0,0897 | 0,7143 | 0,3420
Remote Control | 0,1022 | 0,1376 | 0,3033 | 0,1429 | 0,2261

## Slide 16: Selection of preferred design
Survey analysis -> Panel control
AHP matrix -> Panel control
Preferred design concept -> Panel solution

## Slide 17: System requirement
Stakeholder Requirement | System Requirement | COTS | Classification
Monitor and adjust temperature | Collect temperature data for display and computation | Temperature Sensor, Microcontroller | Must to have
Monitor humidity | Collect humidity data for display and computation | Humidity Sensor, Microcontroller | Must to have
Monitor and adjust CO2-level | Collect CO2-level data for display and computation | CO2 Sensor, Microcontroller | Must to have
Ease of use, Accessibility | Provide UI to interact with user | Touchscreen, Microcontroller | Must to have
Ease of use | UI reaction logic, Communication with sensors, Data calculation, HVAC control signal output. | Microcontroller | Must to have
Adjust indoor environment, Compatibility with existing HVAC system, Ease of deployment | Connect to HVAC controller | 4-Channel Relay Module | Must to have

## Slide 18: System requirement
Stakeholder Requirement | System Requirement | COTS | Classification
Adjust humidity | Increase air humidity | Humidifier | Nice to have
Ease of use | Change the configuration of indoor temperature according to time. | Microcontroller | Nice to have
Energy saving, Ease of use | Automatically switch to economy mode | Motion Sensor | Nice to have
Ease of use | Collect weather information from internet | WIFI module, Weather forecast website | Desirable
Accessibility, Ease of use | To tell information and setting about HVAC system using voice for blind people or people in dark room. | WIFI module, Voice interaction server | Desirable
Cost of implementation | Give user access to get information and setting HVAC system by website. | WIFI module, Website | Desirable
Ease of use | Give user access to get information and setting HVAC system by mobile phone. | WIFI module, Apps | Desirable

## Slide 19: Functional analysis

## Slide 20: Function Block Diagram

## Slide 21: Function Block Diagram

## Slide 22: User Interface

## Slide 23: User Interface

## Slide 24: HW block diagram

## Slide 25: Hardware Components

## Slide 26: Bill of materials (BoM)
BoM table
ITEM | Description | Price US $
1. ARM STM32F103 MCU | Microcontroller | 3
2. ER-TFT070-4 TFT LCD | 7 inch TFT LCD touchscreen | 30
3. 4-Channel Relay | 5V 1-Channel Relay Module | 5
4. 1-Channel Relay | 5V 4-Channel Relay Module | 9
5.DHT11 sensor | Temperature and humidity sensor | 5
6. DS18B20 sensor | Temperature sensor | 10
7.MH-14 sensor | NDIR Infrared CO2 sensor | 79
8.HC-SR501 sensor | PIR motion sensor | 3

## Slide 27: Documents
PM
BRR
SRR
CONOPS
SDR
PDR
CDR
Survey analysis

## Slide 28: Summary

## Slide 29: References